## Slide 1
Summer Project with LBNL
Machine Learning Enabled Multiscale Modeling of Mechanical Deformation of Metal-Matrix-Nanocomposites (MMNC)

## Slide 2
Outline
Problem Background
Scope of Research
Literature Review
Preliminary Work
  Model Creation
  Data Generation/Molecular Dynamics Simulation
  Database creation
  Labelling Defect Mode
  Training Machine Learning Model
    Defect Mode Classification
    Stress Regression Model
  Implementation of Trained Model in Continuum Finite Element
Key Questions and Challenges

## Slide 3
1.0 Problem Background
Metal Matrix Nanocomposites(MMNC)
Example: Al-CNT, Al-SiC, Al-Al2O3 etc
Enhanced Mechanical Properties compared to Micro-composites and Unreinforced Matrix
The reason for this enhancement is attributed to the very high nanoparticle-matrix Interface to volume ratio in these MMNCs
A Multiscale modeling technique is needed that can relate these nanoscale structures with their corresponding macroscale properties

## Slide 4
1.0 Problem Background(2)
Multiscale Modeling
Conventional Hierarchical Multiscale Modeling:
Nanoscale Atomic Model ----> Homogenization---> Equivalent-Continuum-Model(RVE)-->Macroscale Simulation
Mechanical Propertiy of a material is controlled by its most dominant defect, for MMNc the most dominant defect is the nanoparticle and the interface between the nanoparticle and matrix
Conventional homogenization techniques has no way to Incorporate nanoparticle-matrix Interface Mechanisms into the model for the MMNCs
A Possible Remedy, Machine Learning Enhanced Homogenization

## Slide 5
Macro-scale Boundary Value Problem
1. Conservation Laws
2. Kinematics Laws
3. Constitutive Laws
2.0 Scope of Research
ML-Based Multiscale Modeling
(ML-enhanced Homogenization)

## Slide 6
3.0 Literature Review
Xiao S, Hu R, Li Z, Attarian S, Björk K M and Lendasse, A 2020 A machine-learning-enhanced hierarchical multiscale method for bridging from molecular dynamics to continua Neural Comput. Appl. 32 14359–73
Nano-scale(MD)
Macroscale(FEM)
Machine Learning Enhanced Homogenization
Defect Classification Model
Stress Regression Model

## Slide 7
3.0 Literature Review(2)
Xiao S,Phillip Deierling, Saimak Attarian, Ahmed El Tuhami, Machine Learning in multiscale modeling of Spatially Tailored Materails, 2021, Composite and Structures, 249 106511
Additional Feature---> Volume Fraction(VF) of Secondary Phase
Microscale
Macroscale
Spatially Tailored Material(SPT)/
Functionally Graded Materials(FGM)

## Slide 8
3.0 Literature Review(3)
Hyungbum Park, Maenghyo Cho, Multiscale constitutive model using data–driven yield function, Composites Part B: Engineering, Volume 216,2021, 108831, ISSN 1359-8368

## Slide 9
3.0 Literature Review(4)
Dengpeng Huang, Jan Niklas Fuhg, Christian Weißenfels, Peter Wriggers,A machine learning based plasticity model using proper orthogonal decomposition, Computer Methods in Applied Mechanics and Engineering, Volume 365, 2020, 113008
History Dependent Feature
ht

## Slide 10
4.0 Preliminary Work
Software Used:
Atomistic Model Generation --------> LAMMPS and Atomsk
Molecular Dynamics Simulation ----> LAMMPS
Machine Learning and Data Science -------> Tensorflow, Scikit-learn, Pandas, JupyterLab and Jupyter Notebook
Finite Element Model -----------> Code Aster (Through MFront Interface)
Visualization ------> OVITO and Paravis

## Slide 11
4.1 Atomistic Model Creation
Atomsk Script for creating Al-CNT atomistic model
AtomskScript for creating Al-SiC atomistic model
Python Script for automatically creating nanocomposite model of varying particle size

## Slide 12
4.1 Atomistic Model Creation(2)
Resulting Atomistic Models
Pure Aluminum
Al-SiC MMNC
Al-CNT MMNC
Silicon Carbide(SiC)
Carbon NanoTube(CNT)

## Slide 13
4.2 Molecular Dynamic Simulation
Molecular Dynamic(MD) Simulation:
For Pure Aluminum Case, total of 26 MD simulation is performed to generate Machine Learning Trainning Data as follows
Final Axial Loading Condition | Final Shear Loading Condition | Number of Simulation
50% Uniaxial Tension (X and Y direction) | 0%,+20%,-20% | 6
20% Uniaxial Compression (X and Y direction) | 0%,+20%,-20% | 6
50% Bi-axial Tension | 0%,+20%,-20% | 3
20% Bi-axial Compression | 0%,+20%,-20% | 3
20% Bi-axial Tension Compression(X Tension-Y Compression and vis-versa) | 0%,+20%,-20% | 6
No Axial Stress | +20%, -20% | 2
Total |  | 26
Dengpeng Huang et al. ,2020

## Slide 14
4.2 Molecular Dynamic Simulation(2)
LAMMPS Sample Scripts -----> Strain upto 50% Uniaxial Tensile deformation, 20% Shear Deformation

## Slide 15
4.2 Molecular Dynamic Simulation(3)
MD Simulation Result Verification(50% Uniaxial tension at 0% shear)
Xiao el al,2020
Present Simulation Result

## Slide 16
4.3 Database Creation

## Slide 17
4.3 Database Creation(2)

## Slide 18
4.4 Labelling Defect Mode(2)
This defect labelling was done by visualization in OVITO and identifying defect free, dislocation and void modes. An Example is shown in the next page

## Slide 19
4.4 Labelling Defect Mode(3)
OVITO Visualization
Strain State at which dislocation nucleate and onwards
Defect mode labelled: 0
Strain State at which void nucleate and onwards
Defect mode labelled: -1
Strain States before defect nucleation
Defect mode labelled: 1

## Slide 20
4.5 Training Machine Learning Model

## Slide 21
4.5.1 Defect Classification Model

## Slide 22
4.5.1 Defect Classification Model(2)

## Slide 23
4.5.1 Defect Classification Model(3)

## Slide 24
4.5.1 Defect Classification Model(3)

## Slide 25
4.5.2 Stress Regression Model

## Slide 26
4.5.2 Stress Regression Model

## Slide 27
4.5.2 Stress Regression Model

## Slide 28
4.5.2 Stress Regression Model

## Slide 29
4.6 Implementation of ML Machines in FEA
An opensource Finite Element(FE) Solver Code_Aster has been proposed to implement the Molecular Dynamics Learned Machines through an external interface for custmized contitutive equation called "MFront"

## Slide 30
5.0 Key Questions and Challenges
1. The defect mode prediction from the classification model reported in (Xiao el al,2020) is not consistent in the shear direction

## Slide 31
5.0 Key Questions and Challenges
2. Implementation of frame invariance into the Machine Learning Model
3. The database created from the MD simulation result needs to be optimized for better training of ML model. Some data will be much more important than the others. For example, for classification model, data point closer to the decision boundaries are much more important than the other.
4. For the 1D inclusion ie; Al-CNT, Orientation of the CNT will also need to be incorporate into the learning model
5. Molecular Dynamics Simulation stress results has dependency on the strain rate applied. This affect needs to be closely looked into.
6. The interatomic potential of the inclusion and interface needs to be examined closely as, this parameter controls the atomistic information passed to the continuum.